THREE-STAGE SYNCHRONOUS OVERMODULATION CONTROL

OF FIVE-PHASE INVERTERS

V. Oleschuk, G. Griva, R. Prudeak, A. Sizov

Resume. Novel three-stage algorithm of synchronous PWM control of five-phase inverter in the zone of overmodulation has been proposed and investigated. It provides smooth transition from linear modulation range to the ten-step operation mode of five-phase system at the maximum fundamental frequency, with full DC-bus voltage utilization. Simulations give the behavior of five-phase system during synchronous PWM control in the zone of overmodulation.

Keywords: five-phase voltage source inverter, synchronous pulsewidth modulation, increased output frequencies, smooth linear output voltage control.

TREI ETAPE DE REGLARE SINCRONĂ INVERTORUL CU CINCI FAZE

ĬN ZONĂ DE SUPRAMODULARE

V. Olesciuk, G. Griva, R. Prudeak, A. Sizov

Rezumat. Este elaborat şi cercetat un algoritm original de reglare sincronă prin trei etape a invertorului cu cinci faze în zonă de supramodulare, ce asigură trecerea lentă de la zonă modulării lineare la tensiunea fazale de ieşire cu zece trepte a frecvenţei maximale de ieşire a invertorului. Sunt enumărate rezultatele modelarii regimurilor de bază ale funcţionării sistemelor de conversie cincifazate în zonă frecvenţelor majorate de ieşire.

Cuvinte cheie: invertor de tensiune cincifazat, modulaţia impulsurilor în durata sincronă, frecvenţe majorate de ieşire, reglare liniară a tensiunii de ieşire.

ТРЕХЭТАПНОЕ СИНХРОННОЕ РЕГУЛИРОВАНИЕ ПЯТИФАЗНЫХ ИНВЕРТОРОВ В ЗОНЕ СВЕРХМОДУЛЯЦИИ

В. Олещук, Дж. Грива, Р. Прудяк, А. Сизов

Аннотация. Разработан и исследован оригинальный алгоритм синхронного трехэтапного регулирования пятифазного инвертора в зоне сверхмодуляции, обеспечивающий плавный переход от зоны линейной модуляции к десятиступенчатому выходному фазному напряжению на максимальной выходной частоте инвертора. Приведены результаты моделирования базовых режимов работы пятифазной преобразовательной системы в зоне повышенных выходных частот.

Ключевые слова: пятифазный инвертор напряжения, синхронная широтно-импульсная модуляция, повышенные выходные частоты, линейное регулирование выходного напряжения.

INTRODUCTION

Multiphase power electronic converters and ac drives are a subject of increasing interest in the last years due to some advantages compared with standard three-phase systems, especially in the field of high power/current applications. In particular, multiphase topologies of electric drives allow reduction of amplitude and increasing the frequency of torque pulsation, and also reduction of the rotor harmonic losses in electrical machines. Multiphase inverters and converters allow dividing of the controlled power on more inverter legs, reducing the rated current of power switches [1]-[2]. Between different multiphase solutions the more interesting and addressed ones are the five-phase and six-phase power conversion systems [1].

In particular, five-phase adjustable speed drives on the base of five-phase inverters are now ones of the most suitable topologies of multiphase drives for such perspective fields of application, as electric vehicles, ship propulsion, aerospace, etc. So, space-vector-based control and modulation methods and techniques for five-phase systems have been developed intensively during last period [3]-[9]. Five-leg voltage source inverters for five-phase drives are characterised by additional degrees of freedom for their control in comparison with conventional three-phase systems. At the same time it is known, that almost all versions of standard space-vector modulation are based on asynchronous principle, which results in sub-harmonics (of the fundamental frequency) in spectrum of the output voltage of inverters, that are very undesirable in drive systems with increased power rating, operating at low switching frequencies [10],[11].

In order to avoid asynchronism of standard space-vector PWM, novel method of synchronized PWM has been recently proposed and developed for control of three-phase inverters [12], three-level converters [13], open-end winding induction motor drives [14], symmetrical six-phase traction systems [15] (including overmodulation control of split-phase drives [16]), five-phase inverters with operation in linear modulation range [17],[18]. So, this paper present results of the development of this new PWM method for synchronous control of five-phase inverters in the zone of overmodulation.

SYNCHRONIZED SPACE-VECTOR PWM FOR A FIVE-PHASE SYSTEM IN A LINEAR MODULATION RANGE

Basic topology of power circuit of a five-phase voltage source inverter with a star-connected load with the neutral point n is presented in Fig. 1 [7]. In particular, in the case of a five-phase motor as a load, the five stator phases a, b, c, d and e are distributed with a spacing of 720.

Space-vector pulsewidth modulation is one of the most suitable control techniques for five-phase systems. Similar to three-phase space-vector PWM, it can be developed for a five-phase system, as shown in Fig. 2 for a period of the fundamental frequency [8]. In particular, Fig. 2 shows the basic ten large (1, 2, 3, 4, 5, 6, 7, 8, 9, 10) and ten medium (1’, 2’, 3’, 4’, 5’, 6’, 7’, 8’, 9’, 10’) switching vectors for a five-phase inverter in accordance with conventional designation (in brackets) of switching state of every switch of the inverter, where “1” corresponds to the switch-on state of the corresponding switch of the upper group of switches of the phases a - e. This control scheme includes also two zero switching states (00000 and 11111), providing zero voltage at the outputs of the inverter.

Although total number of available voltage space vectors in five-phase inverter is equal to 32, the using only of the mentioned above 22 vectors (ten large and ten medium active vectors, plus two zero vectors) allows minimum number of switchings in inverter and minimum switching losses, combined with good spectrum of the phase-to-neutral voltage [6],[8].

Fig. 1. Topology of a five-phase voltage source inverter [7]

Fig. 2. Basic voltage vectors of five-phase inverter

In order to provide synchronisation of the process of vector PWM, a novel approach has been proposed for synthesis of the output voltage of three-phase inverters [12]. The main principles of this method have been recently developed and modified for synchronous space-vector PWM control of five-phase systems in linear modulation range [17]. In particular, with application to five-phase inverters, one of the basic ideas of the method of synchronized PWM is in continuous synchronization of the positions of all central active switching signals  in the centres of the 360-clock-intervals (to fix positions of the -signals in the centres of the 360-cycles), and then – to generate symmetrically around the centres of the 360-clock-intervals all others active -signals.

It is necessary to take into consideration during this process, that in the linear modulation region the total duration of each -signal consists from four parts (, see Figs. 4-5), corresponding to four voltage vectors (two large vectors and two medium vectors) [6]. So, all these sub-signals, together with notches between the -signals, have to be generated symmetrically around the centres of the 360-clock-intervals too.

To provide continuous synchronization of the output voltage of five-phase inverters, by analogy with three-phase converters [12], the scheme of synchronized PWM includes, as an important control parameter, boundary frequencies Fi, transient between control sub-zones, which are situated on the axis of the fundamental frequency F of the system.

Table I presents basic control functions for five-phase voltage source inverter with synchronized PWM during linear modulation zone, which are compared here with the corresponding PWM functions for standard three-phase inverter. It is assumed, that both three-phase and five-phase systems operate under standard V/F control;  - width of sub-cycle, i - number of notches inside a half of clock-intervals in Table 1.

Basic  Control  Functions  of  Synchronized  Schemes  of  PWM

| Control function | Three-phase inverter | Five-phase inverter |
| --- | --- | --- |
| Modulation index | m= |
| Boundary frequencies transient between control sub-zones |  |  |
| Coefficient of synchronization |  |
| The central active switching state |  |  |
| Active switching states |  |  |
| Border active switching state |  |  |
| The minor part of active switching states |  |  |
| Switch-off states (zero voltages) |  |
| Boundary switch-off state |  |

As an example of operation of five-phase inverter with synchronized PWM in linear modulation range, Fig. 3 presents switching signals (pole voltages Va  - Ve) for the phases a – e, line-to-line voltage Vas and phase-to-neutral voltage Van on a period of the fundamental frequency F.

Fig. 4 and Fig. 5 show more in details switching state sequence and the pole and phase voltages of five-phase inverter for the 2nd and the 3rd control sectors. Switching states correspond here to the designations presented in Fig. 2.

Fig. 3. Basic voltages of five-phase inverter in linear modulation zone

Fig. 4. Switching state sequence and basic voltage waveforms of five-phase inverter with synchronized PWM in the second control sector.

Fig. 5. Switching state sequence and basic voltage waveforms of five-phase inverter with synchronized PWM in the third control sector

As an other example of operation of five-phase inverter with synchronized PWM at the boundary of linear modulation zone, Figs. 6-7 show basic voltage waveforms and spectra of the line and phase voltages of five-phase inverter at the fundamental frequency F=41.3Hz, modulation index m=0.826 in the case of scalar control mode. The switching frequency is 3 kHz.

Fig. 6. Basic voltage waveforms of five-phase inverter at the boundary of linear control range (F=41.3Hz, m=0.826)

Fig. 7. Spectra of line and phase-to-neutral voltages of five-phase system at the boundary of linear control range (F=41.3Hz, m=0.826)

THREE-STAGE CONTROL OF FIVE-PHASE SYSTEM WITH SYNCHRONIZED PWM IN THE OVERMODULATION ZONE

Converters’ control in the zone of overmodulation has some specific peculiarities [19]-[22]. Due to features of five-phase systems, rational PWM control of five-phase inverters in the zone of overmodulation, from the boundary of linear control range until the maximum fundamental voltage (at ten-step control mode) can be based on three-stage control scheme.

Maximum Modulation Index

Modulation index is an important parameter of control scheme of PWM inverters. For power conversion systems with standard scalar V/F=const control, the modulation index m is characterizing both the normalized fundamental voltage and the normalized fundamental frequency. In particular, for five-phase inverters with V/F control the modulation index m is defined as

m= F/Ften-step=V1/V1ten-step                                                    (1)

where V1 is the fundamental voltage, and V1ten-step is the fundamental voltage generated at ten-step operation, which is characterized by the maximum Ften-step fundamental frequency. So, the maximum modulation index m=mten-step=1 can be achieved only at the ten-step operation mode.

The First Stage of Synchronous Overmodulation Control

It is known, that the maximum fundamental peak line-to-neutral voltage of five-phase inverter at ten-step operation is 0.6366Vdc [9]. At the same time it is known, that the maximum achievable peak phase-to-neutral voltage of five-phase system (with high-quality control based on optimal combined application of medium and large space vectors) is limited by 0.5257Vdc [6]. So, in order to obtain linearity of the fundamental voltage versus frequency characteristic of five-phase system with standard scalar control during the whole control range, scaled coefficient equal to 0.6366/0.5257=1.21 should be used in PWM scheme for determination of duration of active switching states (in particular, see the corresponding equation for the basic central active switching state duration  in Table I).

In accordance with (1), the modulation index, corresponding to the boundary of linear control range and the overmodulation zone, can be determined as

mov1 = 0.5257/0.6366 = 0.826                                               (2)

In particular, if the maximum fundamental frequency Ften-step=50Hz, the threshold fundamental frequency , which characterizes the beginning of the zone of overmodulation of five-phase inverter with scalar control, is equal to = mov1 Ften-step=41.3Hz.

The first stage of synchronous overmodulation control of five-phase inverters is characterized by smooth transition from the control scheme, based on combined application of all medium and large space vector (in total 22 vectors, including two zero vectors, are used in this scheme), to the control scheme, based on ten large vectors and two zero vectors. Taking into consideration the fact, that the largest fundamental peak phase-to-neutral voltage, which is characterizing the boundary of this overmodulation sub-zone and corresponds to the radius of the larges circle that can be inscribed within the decagon (see Fig. 2), is equal to 0.6155Vdc [6], the second threshold modulation index in accordance with (1) is determined as

mov2 = 0.6155/0.6366 = 0.967                                            (3)

The second threshold fundamental frequency , which characterizes the upper limit of the first control stage in the zone of overmodulation of five-phase inverter with scalar control (Ften-step=50Hz), is equal to = mov2 Ften-step=48.34Hz.

In order to provide smooth transition to the PWM scheme with ten large space vectors, basic control correlations include during the first overmodulation sub-zone special linear coefficients of overmodulation Kov1 (4), connecting modulation index m with two threshold indices mov1 and mov2

Kov1 = 1- (m – mov1)/( mov2 – mov1)                                         (4)

So, during the first control stage of the overmodulation zone, between the fundamental frequencies  and, a smooth linear decrease of widths of the  and  active signals ([17], see also Table I) is observed in accordance with (5):

(5)

Fig. 8 (F=43Hz, m=0.86) and Fig. 9 (F=46Hz, m=0.92) illustrate smooth synchronous voltage control of five-phase inverter during the first control stage of the overmodulation zone.

Fig. 10 presents basic voltage waveforms of the five-phase inverter with synchronized PWM at the upper boundary of the first stage of inverter control in the zone of overmodulation (F=48.35Hz, m=mov2=0.967). It is necessary to mention, that during all stages of overmodulation control of five-phase inverters there are inevitable distortion of output voltage spectra [6],[9]. But and in this case all presented in Figs. 8-10 voltage waveforms have quarter-wave symmetry during over-modulation control, and its spectra do not contain even harmonics and sub-harmonics, that is especially important for high power/high current applications.

Fig. 8. Pole voltages Va – Vc, line and phase voltages Vac and Van, of five-phase system at the first part of the zone of overmodulation (F=43Hz, m=0.86)

Fig. 9. Pole voltages Va – Vc, line and phase voltages Vac and Van, of five-phase system at the first stage of the zone of overmodulation (F=46Hz, m=0.92).

Fig. 10. Pole voltages Va – Vc, line and phase voltages Vac and Van, of five-phase system at the boundary of the first stage of the zone of overmodulation (F=48.35Hz, m=0.967)

The Second Stage of Synchronous Overmodulation Control

To provide full utilization of the available DC-bus voltage in five-phase systems, it is necessary to carry out smooth transition from the control scheme, based on ten large space vectors application, to the ten-step mode. In this case, the next (second) stage of the overmodulation control is connected with smooth decrease until close to zero values of durations of all notches. By the analogy with three-phase inverters, where value of the corresponding threshold modulation index corresponds to the medium part of the corresponding zone of overmodulation, for five-phase systems the rational value of the third threshold modulation index (and relative value of the third threshold fundamental frequency Fov3) can be determined as: mov3=(mten-step+mov2)/2=(1+0.967)/2=0.984, Fov3= 0.984Ften-step. In particular, if Ften-step=50Hz, Fov3=49.2Hz.

Basic PWM correlations (6) and (7) include special linear coefficient of overmodulation Kov2 (8) in this control sub-zone, connecting modulation index m with the threshold modulation indices mov2 and mov3. So, realization of control functions (6)-(8) provides smooth synchronous decrease of durations of all notches (6) together with simultaneous increasing of widths of the total active –signals (7) until the maximum duration, equal to the duration of sub-cycle .

(6)

(7)

Kov2 = 1- (m – mov2)/( mov3 – mov2)                                            (8)

As an illustration of the PWM control in the second overmodulation sub-zone, Fig. 11 presents basic voltage waveforms of the five-phase inverter with synchronized PWM (F=48.75Hz, m=0.975). The switching frequency is 3kHz.

Fig. 11. Pole voltages Va – Vc, line and phase voltages Vac and Van, of five-phase system at the second stage of the zone of overmodulation (F=48.75Hz, m=0.975)

The Third Stage of Synchronous Overmodulation Control

At the boundary frequency between the second and the last (the third) stage of overmodulation control of five-phase inverter there are no notches between active switching states, and total durations of these –signals include only the -signals like a minor part of total active switching states (see Figs. 4-5). Fig. 12 illustrates this control stage and shows basic voltage waveforms of the modulated five-phase inverter at the third threshold overmodulation frequency (F=Fov3=49.2Hz, m=mov3=0.984).

In order to provide smooth final pulse dropping process of five-phase system with scalar control, with smooth transition from the PWM control mode to the ten-step mode, the third coefficient of overmodulation Kov3 (9) is applied for equations (10)-(11), providing smooth decrease until zero of the widths of the -signals in this control sub-zone:

Kov3=1-(m–mov3)/(mten-step–mov3)=1-(m-mov3)/(1–mov3)                             (9)

(10)

(11)

Fig. 13 shows the pole, line and phase-to-neutral voltages of five-phase system operating in the third sub-zone of the overmodulation region (F=49.6Hz, m=0.992). The switching frequency is 3kHz. The presented voltages have quarter-wave symmetry, and its spectra do not include even harmonics and subharmonics. Fig. 14 presents basic voltage waveforms of five-phase inverter at the maximum fundamental frequency =50Hz, at the ten-step operation mode (m=1).

The proposed algorithm of synchronized modulation of five-phase inverter with standard scalar control mode provides both full utilization of the DC bus voltage in the system and linearity of the fundamental voltage during the whole control range. Fig. 15 illustrates this fact and presents variation of magnitude of the first harmonic of the phase-to-neutral voltage versus modulation index m.

Fig. 12. Pole voltages Va – Vc, line and phase voltages Vac and Van, of five-phase system at the third threshold overmodulation frequency (F=49.2Hz, m=0.984)

Fig. 13. Pole voltages Va – Vc, line and phase voltages Vac and Van, of five-phase system at the third stage of the zone of overmodulation (F=49.6Hz, m=0.992)

Fig. 14. Pole voltages Va – Vc, line and phase voltages Vac and Van, of five-phase system at the ten-step operation mode (F=50Hz, m=1)

Fig. 15. Magnitude of the fundamental phase-to-neutral voltage versus modulation index of five-phase inverter with synchronized PWM

IV.	 CONCLUSION

Novel three-stage algorithm of synchronous PWM control of five-phase inverter in the zone of overmodulation has been proposed and investigated. It provides smooth transition from linear modulation range to the ten-step operation mode of five-phase system at the maximum fundamental frequency. The presented control scheme provides both full utilization of the DC-bus voltage of the system at the maximum fundamental frequency and linearity of the fundamental voltage during the whole control range. The spectra of the phase-to-neutral voltage of five-phase power conversion systems with algorithms of synchronized PWM do not contain even harmonics and sub-harmonics in the zone of overmodulation, which is especially important for high power/high current applications.

REFERENCES

[1]	R. Bojoi, F. Farina, F. Profumo and A. Tenconi, “Dual-three phase induction machine drives control – a survey,” CD-ROM Proc. of the 2005 IEEE Int’l Power Elect. Conf., 10 p.

[2]	R. Bojoi, A. Tenconi, F. Farina and F. Profumo, “Dual-source fed multiphase induction motor drive for fuel cell vehicles: topology and control,” Proc. of the 2005 IEEE Power Electr. Spec. Conf., pp. 2676-2683.

[3]	H.A. Toliyat, “Analysis and simulation of five-phase variable-speed induction motor drives under asymmetrical connections,” IEEE Trans. on Power Electr., vol. 13, no. 4, 1998, pp. 748-756.

[4]	R. Shi and H.A. Toliyat, “Vector control of five-phase synchronous reluctance motor with space vector pulse width modulation (SVPWM) for minimum switching losses,” Proc. of the 2002 IEEE Appl. Power Electr. Conf., pp. 57-63.

[5]	H. Xu, H.A. Toliyat and L.J. Peterson, “Five-phase induction motor drives with DSP-based control system,” IEEE Trans. on Power Electr., vol. 17, no. 2, 2002, pp. 524-533.

[6]	A. Iqbal and E. Levi, “Space vector modulation schemes for a five-phase voltage source inverter,” CD-ROM Proc. of the 2005 European Power Electr. Conf., 12 p.

[7]	A. Iqbal, E. Levi, M. Jones and S.N. Vukosavic, “Generalised sinusoidal PWM with harmonic injection for multi-phase VSIs,” CD-ROM Proc. of the 2006 IEEE Power Electr. Spec. Conf., 7 p.

[8]	H.M. Ryu, J.H. Kim and S.K. Sul, “Analysis of multiphase space vector PWM based on multiple d-q spaces concept,” IEEE Trans. on Power Electr., vol. 20, no. 6, 2005, pp. 1364-1371.

[9]	A. Iqbal, S. Moinuddin and M.R. Khan, “Space vector model of a five-phase voltage source inverter,” Proc. of the 2006 IEEE Int’l Conf. on Ind. Technology, pp. 488-493.

[10]	J. Holtz, “Pulsewidth modulation for electronic power conversion,” Proc. of IEEE, vol. 82, no. 8, 1994, pp. 1194-1213.

[11]	N. Mohan, T.M. Undeland and W.P. Robbins, Power Electronics, 3rd ed., John Wiley & Sons, 2003.

[12]	V. Oleschuk and F. Blaabjerg, “Direct synchronized PWM techniques with linear control functions for adjustable speed drives,” Proc. of the 2002 IEEE Appl. Power Electr. Conf., pp. 76-82.

[13]	V. Oleschuk, B.K. Bose and Zhe Chen, “Synchronized overmodulation techniques for the neutral-clamped inverters,” Proc. of the 2003 IEEE Power Electr. Spec. Conf., pp. 41-46.

[14]	V. Oleschuk, V. Ermuratski, F. Profumo, A. Tenconi, R. Bojoi and A.M. Stankovic, ‘’Novel schemes of synchronous PWM for dual inverter-fed drives with cancellation of zero sequence currents’’, Proc. of the 2006 Int’l Symp. on Power Electronics, Electric Drives, Automation and Motion, pp. 451-456.

[15]	G. Griva, V. Oleschuk and F. Profumo, “Hybrid traction drive with symmetrical split-phase motor controlled by synchronised PWM,” Proc. of the 2008 IEEE Int’l Symp. on Power Electronics, Drives, Automation and Motion,  pp. 1033-1037.

[16]	G. Griva, V. Oleschuk and F. Profumo, “Synchronized overmodulation techniques for symmetrical dual three-phase converters,” Proc. of the 2008 IEEE Int’l Symp. on Power Electronics, Drives, Automation and Motion, pp. 981-986.

[17]	V. Oleschuk, F. Profumo, A. Tenconi and E. Yaroshenko, “Five-phase inverters with synchronized PWM,” Proc. of the 2007 IEEE EUROCON Conf., pp. 1872-1878.

[18]	V. Oleschuk, F. Profumo and A. Tenconi, “Simplifying approach for analysis of space-vector PWM for three-phase and multiphase converters,” CD-ROM Proc. of the 2007 Europ. Power Electr. Conf., 10 p.

[19]	J. Holtz, V. Lotzkat and A.M. Khambadkone, “On continuous control of PWM inverters in the overmodulation range including the six-step mode,” IEEE Trans. on Power Electr., vol. 8, no. 4, 1993, pp. 546-553.

[20]	G. Griva, T.G. Habetler, F. Profumo and M. Pastorelli, “Performance evaluation of a direct torque controlled drive in the continuous PWM-square wave transition region,” Proc. of the 1993 IEEE Power Electr. Spec. Conf., pp. 237-244.

[21]	S.K. Mondal, B.K. Bose, V. Oleschuk and J.O.P. Pinto, “Space vector pulse width modulation of three-level inverter extending operation into overmodulation region,” IEEE Trans. on Power Electr., vol. 18, no. 2, 2003, pp. 604-611.

[22]	V. Oleschuk, V. Ermuratski and E.M. Chekhet, “Drive converters with synchronized pulsewidth modulation during overmodulation,” Proc. of the 2004 IEEE Int’l Symp. on Ind. Electr., pp. 1339-1344.

Valentin Oleschuk, Dr. of Sc., is working in the Power Engineering Institute of the Academy of Sciences of Moldova from 1971. He is author and co-author of two books and more than 230 publications in the area of power electronics and electric drives, including more than 60 IEEE publications. He is also the author of 89 patents and authors certificates in this field. His research interests include control and modulation strategies for perspective topologies of power converters, drives and renewable energy systems.

Giovanni Griva, PhD, is Associate Professor of the Politecnico di Torino, Turin, Italy. He is author and co-author of more than 100 technical papers published in international journals and proceedings of international conferences. His scientific interests regard power conversion systems, adjustable speed electric drives and non conventional actuators.

Roman Prudeak is PhD Student of the Power Engineering Institute of the Academy of Sciences of Moldova. He is author of several technical papers in the field of power electronics and electric Drives. His research interests include both feedforward and feedback control methods and techniques for power converters and drives.

Alexandr Sizov is Scientific Collaborator of the Power Engineering Institute of the Academy of Sciences of Moldova. He is author and co-author of more than 60 publications and 10 patents and authors certificates. His research interests include elaboration, modelling and simulation of control algorithms and control systems for power electronic converters and electric drives.